# EMScope JavaScript API
JavaScript client library for the EMScope EMI measurement instrument (SW ≥ 4.1).
This is the browser counterpart of the Python api_v5.py client and follows the exact same wire protocol. Refer to the WebSocket API documentation for the full protocol description.
## Legacy API — Software ≤ 3.13
The api.js and api_example.html files are provided for use with EMScope software versions 3.13 and earlier.
Required: a modern browser with native WebSocket support.
## Current API — Software ≥ 4.1
The api_v5.js and api_example_v5.html files are provided for EMScope software version 4.1 and later.
Include api_v5.js in your HTML page. No external dependencies are required for browser use. Under Node.js, install the ws package and pass it via the WebSocketImpl option (see below).
The example file api_example_v5.html is a self-contained browser application with a live spectrum plot, configuration panel, and message log. Open it directly in a browser after setting the instrument IP address.
### Connection model
Unlike the Python client (which uses an explicit receive loop), the JavaScript client is event-driven. The WebSocket connection opens automatically when the object is constructed. All incoming messages are delivered via the callback.
### RBW / frequency bands
Value	RBW	Frequency range	Standard
200	200 Hz	9 kHz – 150 kHz	CISPR 16-1-1
9	9 kHz	150 kHz – 30 MHz	CISPR 16-1-1
120	120 kHz	30 MHz – 110 MHz	CISPR 16-1-1
1	1 kHz	10 kHz – 150 kHz	MIL-STD-461
10	10 kHz	150 kHz – 30 MHz	MIL-STD-461
200_9	dual	9 kHz – 30 MHz	CISPR dual-band
1_10	dual	10 kHz – 30 MHz	MIL dual-band

### Node.js
The library is compatible with Node.js. Install the ws package and pass it as the WebSocket implementation via the constructor options. See the source file for details.